## Slide 1: Internet of Things
Dr. Raihan Ul Islam
Associate Professor
Department of Computer Science & Engineering
Room No# AB3-1003 Email: raihan.islam@ewubd.edu
Mobile: +8801992392611

## Slide 2: What is REST ?
REST means
REpresentational
State
Transfer

## Slide 3: REpresentational ? State ? Transfer ?
It represent the state of database at a time. But how???
REST is an architectural style which is based on web-standards and the HTTP protocol.
In a REST based architecture everything is a Resource.
A resource is accessed via a common interface based on the HTTP standard methods.
You typically have a REST server which provides access to the resources and a REST client which accesses and modifies the REST resources.

## Slide 4: REpresentational ? State ? Transfer ?
Every resource should support the HTTP common operations.
Resources are identified by global IDs (which are typically URIs or URLs).
REST allows that resources have different representations, e.g., text, XML, JSON etc.
Stateless in nature. Excellent for distributed system.
Stateless components can be freely redeployed if something fails, and they can scale to accommodate load changes.
This is because any request can be directed to any instance of a component.

## Slide 5: HTTP Methods
The PUT, GET, POST and DELETE methods are typically used in REST based architectures. The following table gives an explanation of these operations:
HTTP Method | CRUD Operation | Description
POST | INSERT | Addes to an existing resource
PUT | UPDATE | Overrides existing resource
GET | SELECT | Fetches a resource. The resource is never changed via a GET request
DELETE | DELETE | Deletes a resource

## Slide 6: Architecture:

## Slide 7: HTTP Request Example:

## Slide 8: HTTP Response Example:

## Slide 9: HTTP REST Request:
HTTP REST API Request
GET https://www.myhost.com/api/v1/user/1/cities
Read, All the cities for user whose id is 1
GET /user/1/cities http/1.1
host: https://www.myhost.com/api/v1
Content-Type: application/json
Accept-Language: us-en
state_id: 2

## Slide 10: HTTP REST Response:
HTTP REST API Response
HTTP/1.1 200 OK (285ms)
Date: Fri, 21 Apr 2017 10:27:20 GMT
Server: Apache/2.4.6 (CentOS) OpenSSL/1.0.1e-fips PHP/7.0.16
X-Powered-By: PHP/7.0.16
Content-Length: 109
Keep-Alive: timeout=5, max=100
Connection: Keep-Alive
Content-Type: application/json; charset=UTF-8
{"status":"success","message":"City List","data":[{"city_name":"Visakhapatnam"},{"city_name":"Vijayawada"}]}

## Slide 11: HTTP Response Status Code:
1xx | Inform­ational Codes
2xx | Successful Codes
3xx | Redire­ction Codes
4xx | Client Error Code
5xx | Server Error Codes
List at here: https://en.wikipedia.org/wiki/List_of_HTTP_status_codes

## Slide 12: Points to be noted
For REST APIs

## Slide 13: Use Nouns but no verbs in path/URI:
Purpose | Method | Incorrect | Correct
Retrieves a list of users | GET | /getAllCars | /users
Create a new user | POST | /createUser | /users
Delete a user | DELETE | /deleteUser | /users/10
Get balance of user | GET | /getUserBalance | /users/11/balance

## Slide 14: Use plural nouns:
Do not mix up singular and plural nouns. Keep it simple and use only plural nouns for all resources.
/cars instead of /car /users instead of /user /products instead of /product /settings instead of /setting

## Slide 15: GET method should not alter the state:
Use PUT, POST and DELETE methods instead of the GET method to alter the state.
Do not use GET method or Query parameters for state changes:
GET /users/711?activate or
GET /users/711/activate

## Slide 16: Use sub-resources for relation:
If a resource is related to another resource use subresources
GET /cars/711/drivers/ (Returns a list of drivers for car 711)
GET /cars/711/drivers/4 (Returns driver #4 for car 711)

## Slide 17: Use HTTP headers for serialization formats:
Both, client and server need to know which format is used for the communication. The format has to be specified in the HTTP-Header.
Content-Type defines the request format.
Accept defines a list of acceptable response formats.

## Slide 18: Versioning is important:
Make the API Version mandatory and do not release an unversioned API.
Use a simple ordinal number and avoid dot notation such as 2.5
We are using the url for the API versioning starting with the letter “v”
/blog/api/v1

## Slide 19: Handle Errors with HTTP Status code:
200 | OK (Everything is working) | 403 | Forbidden (The server understood the request, but is refusing it or the access is not allowed)
201 | OK (New resource has been created) | 404 | Not found (There is no resource behind the URI)
204 | OK (Resource successfully deleted) | 405 | Method not allowed
400 | Bad Request (The request was invalid or cannot be served. The exact error should be explained in the error payload. E.g. „The JSON is not valid“) | 408 | Request timeout
401 | Unauthorized (The request requires an user authentication) | 500 | Internal server error

## Slide 20: Filtering:
Use a unique query parameter for all fields or a query language for filtering.
    GET /cars?color=red (Returns a list of red cars)
    GET /users?name=tom (Returns a list of users whose name matches tom)

## Slide 21: Sorting:
Allow ascending and descending sorting over multiple fields.
GET /cars?sort=-manufacturer,+model
This returns a list of cars sorted by descending manufacturers and ascending models)

## Slide 22: Paging:
Use limit and offset. It is flexible for the user and common in leading databases.
The default should be limit=20 and offset=0
GET /cars?offset=10&limit=5

## Slide 23: Aliases for common queries:
To make the API experience more pleasant for the average consumer, consider packaging up sets of conditions into easily accessible RESTful paths.
For example consider following use case:
POST /users (User Register: Creates a new user)
POST /users/login (User Login: Creates auth token for user authentication)

## Slide 24: Want to develop REST APIs easily???
Checkout Slim - A microframework for php.
Documentation: https://www.slimframework.com/docs/

## Slide 25: Introduction To CoAP
The Constrained Application Protocol (CoAP) is a specialized web transfer protocol for use with constrained devices(such as microcontrollers) and constrained networks in the Internet of Things.
This protocol is designed for machine-to-machine (M2M) applications such as smart energy and building automation.

## Slide 26: Architecture Of CoAP
It is specified in RFC 7252.It is open IETF standard
It is very efficient RESTful protocol.
Easy to proxy to/from HTTP.
It is Embedded web transfer protocol
It uses asynchronous transaction model.
UDP is binding with reliability and multicast support.
GET, POST, PUT and DELETE methods are used.
uses subset of MIME types and HTTP response codes.
Uses built in discovery mechanism.

## Slide 27: Architecture Of CoAP
URI is supported.
It uses small and simple 4 byte header.
Supports binding to UDP, SMS and TCP.
DTLS based PSK, RPK and certificate security is used.

## Slide 28: CoAP Structure
There are two different layers that make CoAP protocol:
1)Messages
2)Request/Response.
The Messages layer deals with UDP and with asynchronous messages.
The Request/Response layer manages request/response interaction based on request/response messages.

## Slide 29: CoAP Structure
Message layer supports 4 types of messages:
  Confirmable
  Non-confirmable
  Acknowledgment
  Reset
Message layer is meant for Re-transmitting lost packets. Request/Response layer contains methods like GET,PUT,POST and DELETE.

## Slide 30: Common Terms in CoAP
Client: The entity that sends a request and the destination of the response
Server: The entity that receives a request from a client and sends back a response to the client
Endpoint: An entity that participates in the CoAP protocol. Usually, an Endpoint is identified with a host
Sender: The entity that sends a message
Recipient: The destination of a message

## Slide 31: CoAP Messages Model
This is the lowest layer of CoAP.
This layer deals with UDP exchanging messages between endpoints.
Each CoAP message has a unique ID; this is useful to detect message duplicates.
The CoAP protocol uses two kinds of messages:
  Confirmable message - this is a reliable message.
  Non-confirmable message-this are unreliable messages.

## Slide 32: CoAP Messages Model
In CoAP, a reliable message is obtained using a Confirmable message (CON).
A Confirmable message is sent again and again until the other party sends an acknowledge message (ACK). The ACK message contains the same ID of the confirmable message (CON).

## Slide 33: CoAP Messages Model
if the server has troubles managing the incoming request, it can send back a Rest message (RST) instead of the Acknowledge message (ACK)

## Slide 34: CoAP Messages Model
The other message category is the Non-confirmable (NON) messages. These are messages that don’t require an Acknowledge by the server.
They are unreliable messages or in other words messages that do not contain critical information that must be delivered to the server.
To this category belongs messages that contain values read from sensors.
Even if these messages are unreliable, they have a unique ID.

## Slide 35: CoAP Request/Response Model
The CoAP Request/Response is the second layer in the CoAP abstraction layer.
The request is sent using a Confirmable (CON) or Non-Confirmable (NON) message.
There are several scenarios depending on if the server can answer immediately to the client request or the answer if not available.

## Slide 36: CoAP Request/Response Model
If the server can answer immediately to the client request, then if the request is carried using a Confirmable message (CON), the server sends back to the client an Acknowledge message containing the response or the error code.
The Token is different from the Message-ID and it is used to match the request and the response.

## Slide 37: CoAP Request/Response Model
If the server can’t answer to the request coming from the client immediately, then it sends an Acknowledge message with an empty response.
As soon as the response is available, then the server sends a new Confirmable message to the client containing the response.
At this point, the client sends back an Acknowledge message:

## Slide 38: CoAP Message Format
Where:
Ver: It is a 2 bit unsigned integer indicating the version
T: it is a 2 bit unsigned integer indicating the message type: 0 confirmable, 1 non-confirmable
TKL: Token Length is the token 4 bit length
Code: It is the code response (8 bit length)
Message ID: It is the message ID expressed with 16 bit
And so on.

## Slide 39: CoAP Security Aspects
CoAP uses UDP to transport information. CoAP relies on UDP security aspects to protect the information.
As HTTP uses TLS over TCP, CoAP uses Datagram TLS over UDP. DTLS supports RSA, AES, and so on.
Anyway, we should consider that in some constrained devices some of DTLS cipher suits may not be available.
It is important to notice that some cipher suites introduces some complexity and constrained devices may not have resources enough to manage it.

## Slide 40: MQTT
▶ MQTT is described on the mqtt.org site as a machine-
to-machine (M2M) / IoT connectivity protocol.
▶ MQTT is an Event based IoT middleware (one to many)
▶ publish/subscribe messaging transport protocol
▶ Over TCP/IP (or MQTT-S over UDP for LAN)
▶ Its protocol is lightweight
▶ it can be supported by some of the smallest measuring
and monitoring devices (ex. Arduino)
▶ it can transmit data over far reaching networks
▶ It can transmit data over sometimes intermittent networks.
Event based IoT Middleware
Event pattern of communication (one to many)
Over IP (TCP)

## Slide 41: Publish / Subscribe Messaging (One to Many)
▶ A producer publishes a message (publication) on a topic (subject)
▶ A consumer subscribes (makes a subscription) for messages on a topic (subject)
▶ A message server (called BROKER) matches publications to subscriptions
▶ If none of them match the message is discarded after modifying the topic
▶ If one or more matches the message is delivered to each matching consumer after
modifying the topic
▶ Publish / Subscribe has three important characteristics:
It decouples message senders and receivers, allowing for more flexible applications
It can take a single message and distribute it to many consumers
This collection of consumers can change over time, and vary based on the nature of the message.
Server

## Slide 42: MQTT Topic and Wildcards

## Slide 43: MQTT Topic : Details
A topic forms the namespace
▶ Is hierarchical with each “sub topic” separated by a /
▶ An example topic space
▶ A house publishes information about itself on:
▶ <country>/<region>/<town>/<postcode>/<house>/energyConsumption
▶ <country>/<region>/<town>/<postcode>/<house>/solarEnergy
▶ <country>/<region>/<town>/<postcode>/<house>/alarmState
▶ <country>/<region>/<town>/<postcode>/<house>/alarmState
▶ And subscribes for control commands:
▶ <country>/<region>/<town>/<postcode>/<house>/thermostat/setTemp
A subscriber can subscribe to an absolute topic or can use wildcards:
▶ Single-level wildcards “+” can appear anywhere in the topic string
▶ Multi-level wildcards “#” must appear at the end of the string
▶ Wildcards must be next to a separator
▶ Cannot be used wildcards when publishing
▶ For example
▶ UK/Hants/Hursley/SO212JN/1/energyConsumption
▶ Energy consumption for 1 house in Hursley
▶ UK/Hants/Hursley/+/+/energyConsumption
▶ Energy consumption for all houses in Hursley
▶ UK/Hants/Hursley/SO212JN/#
▶ Details of energy consumption, solar and alarm for all houses in SO212JN

## Slide 44: MQTT publish subscribe architecture
▶ The MQTT messages are delivered asynchronously (“push”) through publish subscribe architecture.
▶ The MQTT protocol works by exchanging a series of MQTT control packets in a defined way.
▶ Each control packet has a specific purpose and every bit in the packet is carefully crafted to reduce the data transmitted over the network.
▶ A MQTT topology has a MQTT server and a MQTT client.
▶ MQTT client and server communicate through different control packets. Table below briefly describes each of these control packets.

## Slide 45: Sample of protocol use

## Slide 46: Ideal for constrained networks (low bandwidth, high latency, data limits, and fragile connections)
▶ MQTT control packet headers are kept as small as possible.
▶ Each MQTT control packet consist of three parts, a fixed header, variable header and payload.
▶ Each MQTT control packet has a 2 byte Fixed header. Not all the control
packet have the variable headers and payload.
▶ A variable header contains the packet identifier if used by the control packet.
▶ A payload up to 256 MB could be attached in the packets.
▶ Having a small header overhead makes this protocol appropriate for IoT by
lowering the amount of data transmitted over constrained networks.

## Slide 47: Quality of Service (QoS) for MQTT
▶ Quality of service (QoS) levels determine how each MQTT message is
delivered and must be specified for every message sent through MQTT.
▶ Three QoS for message delivery could be achieved using MQTT:
▶ QoS 0 (At most once) - where messages are delivered according to the best efforts of the operating environment. Message loss can occur.
▶ QoS 1 (At least once) - where messages are assured to arrive but duplicates can occur.
▶ QoS 2 (Exactly once) - where message are assured to arrive exactly once.
▶ There is a simple rule when considering performance impact of QoS : “The higher the QoS, the lower the performance".

## Slide 48: Quality of Service (QoS) for MQTT

## Slide 49: MQTT Clients and APIs
▶ You can develop an MQTT client application by programming directly to the MQTT protocol specification …… however it is more convenient to use a prebuilt client
▶ Open Source clients available in Eclipse Paho project
▶ C, C++, Java, JavaScript, Lua, Python and Go
▶ Clients for other languages are available, see mqtt.org/software
▶ E.g. Delphi, Erlang, .Net, Objective-C, PERL, PHP, Ruby
▶ Not all of the client libraries listed on mqtt.org are current. Some are at an early or experimental stage of development, whilst others are stable and mature.
▶ Even in shell script like we are seeing in the practical course …

## Slide 50: Thanks to
An Introduction to REST API -Aniruddh Bhilvare
CoAP-Constrained Application Protocol - SHAIK SABAHAT NOWREEN

## Slide 51
Thank you